## Slide 1: STM32-Based Home Safety & Theft Detection System

## Slide 2: Objective
To design a compact embedded system using STM32 that detects intrusion, smoke, and high-temperature fire conditions with priority-based alarm handling for home safety.

## Slide 3
SYSTEM COMPONENTS
Microcontroller: STM32 (F4 series)
Sensors:
  PIR Sensor – Intrusion detection
  MQ-2 Gas Sensor – Smoke/Gas detection
  LM35 Temperature Sensor – Fire / over-temperature detection
Outputs:
  Buzzer (audible alerts)
  LEDs (status indication)
Communication: UART (system status/debug)
When a dangerous condition is detected, the STM32 sends a text alert via UART, for example:
FIRE ALERT: HIGH TEMPERATURE DETECTED
SMOKE ALERT: SMOKE LEVEL HIGH
INTRUSION ALERT: MOTION DETECTED

## Slide 4
System Working
PIR sensor triggers EXTI interrupt on motion detection
MQ-2 sensor output is monitored via ADC for smoke detection
LM35 temperature sensor is read using ADC for over-temperature detection
Sensor values are compared against predefined thresholds
Alarm is activated based on event priority
System status is sent via UART
Priority Order
High temperature (fire) – highest priority
Smoke detection – medium priority
Motion detection – lowest priority

## Slide 5
PIR Sensor ──> EXTI
│
MQ-2 Sensor ─> ADC ─┼─> STM32 ──> Buzzer
│ LEDs
LM35 Sensor ─> ADC
└──> UART → PC
Sensor | What it does
PIR | EXTI interrupt → sets motion_flag = 1
MQ-2 | ADC reading crosses threshold → smoke_flag = 1
LM35 | ADC reading crosses threshold → temp_flag = 1

## Slide 6
if (temp_flag)
{
fire_alarm(); // Highest priority given if all three events occur at same time
}
else if (gas_leakage_flag)
{
gas_leakage_alarm();
}
else if (motion_flag)
{
intrusion_alarm();
}